## Slide 1
NETCPS REU
August 2, 2019
Charlie Broadbent | Faculty Mentor: Dr. Vinod Namboodiri
The Problem
Processing time for very large images between the two tools also varies greatly (up to 37 minutes vs. IBeaconMap’s 3 minutes).
Since the base functionality of the program needs to locate the doors on a floor plan, this is what I set out to achieve. Therefore, we want a tool that:
Marks as many doors on a floor plan as possible without missing any.
  At the same time, it should make as many least redundant marks as possible (i.e. marks that are not doors).
Is simple to use for a person of any level of computer experience.
What are the goals of this tool?
Results
For the most part, it is accurate, though slightly less than IBeaconMap.
When setting up a building for indoor navigation, one of the first steps is deciding on where to place Bluetooth beacons that will be used to transmit navigational information to users.
How does it work?
First, we run a feature detection algorithm (I chose SIFT) on an image of the floor plan and a cropped image of a door from the same floor plan.
What improvements need to be made?
Indoor Navigation for the Blind:
Processing Digital Floor Plans Using OpenCV-Python for Beacon Placement
How can we automate this?
SIFT
Floor plan with all features marked
k-means clustering
Brute-force checker
If the floor plan has a lot of curves, they can be detected to be doors.
 | Doors found | Missed doors | Redundant points | Processing time (s)
Shopping Mall | 49 | 0 | 27 | 5.38
Sample plan (low res) | 16 | 2 | 16 | 1.33
Research Building | 50 | 7 | 27 | 3.18
Large Area | 208 | 18 | 204 | 2247
IBeaconMap’s results (lower table). The research building, shopping mall, and large area floor plans used were the same images for both programs. FDM indicates the use of only feature detection and no machine learning.
Final result
Matched features
Perhaps the simplest way to do this is to manually have someone look over a floor plan; however, this can be time consuming, and prone to human-error, especially with very large floor plans.
OpenCV, a library of programming functions, is an alternative for implementing computer vision.
What if there was a tool to allow us to automate this process? Luckily, there is: IBeaconMap. The problem is it that it is written in MATLAB, which means it cannot be distributed without a fee.
Using OpenCV (specifically, the Python libraries), can we create a software similar to IBeaconMap that is just as accurate?
This gives us a set of keypoints and descriptors. We then match the features from the floor plan to the features of the door. This leaves us with the features in the floor plan that are most likely part of a door.
Feature matching does not work perfectly, however. It leaves is with many more points than we need, and we need to somehow reduce these points down to a single point that is on top of a door
We can make a significant reduction using k-means clustering, which will find the centers of some clusters of keypoints, but not all, meaning we must reduce further.
We reduce the rest of the points by checking if other points exist within a certain radius. If there exists such a point, we add a new point at the midpoint. This process continues until all points are sufficiently far away from each other.
The leftover points are not perfectly placed, and there will exist redundant points—so how accurate is this process?
The UI is barebones, but very simple.
Better UI
A more efficient clustering algorithm and/or data structure to store keypoints to improve processing time on large images.
Improved optimization of OpenCV’s feature detection, feature matching, and clustering algorithms to improve accuracy and reduce redundancy.
UI